## Slide 1: Controlled Battery discharge system
Industrial electronics and instrumentation course a.a. 2017/2018
Department of Industrial engineer
Cristiano Strobbe
I.D. 196763

## Slide 2: Introduction
The goal of this project was to build an instrument that identifies the electrical/thermal parameters of a Li-Ion cell’s model.
The model are then used to estimate the SoC (State of Charge) of a battery for a Formula SAE car.
The identification process can be done in several ways, the one that I choose was using discharge pulses.
The requirements for this instrumentation were:
Be able to discharge at least one battery module with different current profiles (pulse, ramp etc.).
High discharge current (almost 240A – Full car throttle)
Cheaper as possible (1000 euros budget)
Acquire and store batterie’s voltages, batterie’s temperature and total current at a reasonable speed (at best 150 Hz).

## Slide 3: Battery module
The battery pack is composed by several modules, in my case Energus 6p1s Sony VTC5.
Just rough calculations, if I want to discharge the module at 200A (assuming nominal voltage) I need to dissipate 720 W.
Capacity: 15.6 Ah
Nominal voltage: 3.6V
Maximum voltage: 4.2V
Cut-off voltage: 2.5V
Max discharge current: 280A (5s pulse)
Max continuous discharge current: 180A
Notes: Let’s start by looking at the battery parameters

## Slide 4: On Market solutions
There are two ways in which the test can be done: using programmable DC loads as:
or can be obtained using very expensive and sophisticated instrumentations (HPPC test instrument)
BK 8600 Series
Max load voltage: 60V-120V
Current: up to 240A
Built-in DAS
Price: 4000$-10000$
Neware CT-4002
Load voltage: 0.025V-5V
Current: up to 300A
Built-in DAS
Price: > 10000$

## Slide 5: Constant current load
The easiest and cheaper solution that I found was to use the so called ”constant current load”, here the schematic
The basic principle is that the voltage that I apply on the inverting side of the Op-amp is the same that I apply between the resistor’s terminals.
So, if I use a 0.1 Ohm resistor and I apply one Volt as reference voltage the current that flows through the battery, the NMOS and the resistor is 10A.
Notes: As first thing I created a small constant current and tried to discharge a single Samsung 18650-25R at 15A. The results were good so I started with the design of the bigger one. For this part I used LTSpice for simulating the entire circuit.

## Slide 6: Final circuit diagram
After a long time spent on LTSpice I finally reach the final circuit. The main problems that I found were:
Parallels of mosfets are difficult to manage (parameters mis-matching)
Heat dissipation
Op-amp oscillating behaviour
Finding electrical components which were able to meet my requirements
Notes: Parallel of mosfets

## Slide 7: LTSPice schematic
Here the schematic of one of the five circuit’s section:
Noise injection
Standard operational amplifier
Power mosfets
Power resistor
Battery simulator
Reference voltage simulator

## Slide 8: Heat dissipation
From the simulation I found the power that the mosfets and the resistors have to dissipate. Here 2 simulations which show how the current drawn varies with respect to the reference voltage and how the heat power vary with respect to the current draw.
A cooling system was needed.
(Blue: reference voltage Green: current drawn per section)
(Green: mosfet’s power Red: resistor’s power)
Notes: As shown for low currents most of the power goes inside the resitor (power peak of) while for higher currents are the mosfets that dissipate most of the power.
so I started looking on the market which kind of solution is better. In order to correctly design the cooling I choose the maximum power dissipate for each device. This idea is conservative (explain better)

## Slide 9: Power Components
The power components were:
10x Mosfet IXIS IXFK360N10T
Rds of 2.9 mOhm
Vdss 100V
Idmax 360A
Pmax 1250 W
Rthjc 0.12W/°C
Rthcs 0.05 W/°C
Vgs(th) 2.5V-4.5V
5x 0.1Ohm +/-5% Arcol HS200 R1 J
200W power rating
50W without cooling

## Slide 10: Busbar design
Thanks to ProM I was able to design my own busbar starting from a cupper sheet of 1.5mm thickness. For the design/simulation I used a well known 1DoF thermal model implemented using Matlab, here the final simulation of the positive busbar (1.5m length).

## Slide 11: Final result
Cooling system
Batteries and almost adiabatic case
Reference generator
Resistor’s
cooling
Control board

## Slide 12: Data logger - Hardware
NI USB-6008
NI cDAQ-9181
USB connection
Up to 8 Differential ADC
+/- 10V range
12 bit of resolution
10 KS/s
TCP/IP connection
Up to 4 Differential ADC
+/- 10V range
16 bit of resolution
100 KS/s
Both the devices were used in differential mode.

## Slide 13: Data logger - software
After choosing and setting the hardware I created the VI which logs and plots all the data. This VI can be used with both hardware.
User interface
Code

## Slide 14: sensors
DHAB-S24 Hall effect current sensor
Single 5V supply
+/- 500A of current range
4mV per Ampere of sensitivity
10K NTC Thermistor B3380 Cantherm
+/- 1% of tolerance
Time constant < 3 seconds
Already wired up

## Slide 15: conclusion: Data analysis
Here a slice of a discharge test at 120A sampled at 50 Hz and with a resolution of 3mV.
Batteries
voltages
Current

## Slide 16: conclusion: Data analysis pt.2
Here the FFT of the current during the discharge pulse without any filtering.
DC component
White noise
Fs = 50 Hz
Resolution = 3mV

## Slide 17: Thanks for the attention